## Slide 2: What Winlink offers for EMCOMM
Flexibility:
  Internet-only (Telnet) direct connections to Winlink.
  Radio link bridge to Internet e-mail.
  Radio-only store and forward messaging.
  Peer-to-peer connections between radio end-users.
  Familiar and simple e-mail client interface.
Interoperability: Connect different types of systems
  Bridge different radio capabilities (VHF/UHF/HF).
  Seamless integration with Internet e-mail.
Geographical dispersion and redundancy for reliability

## Slide 3: What Winlink offers for EMCOMM (more)
Standard e-mail format with many features.
  Binary file attachments (pictures, pdf, spreadsheets).
  Automatic message compression/decompression.
  White listing used to prevent spam.
Time independence.
Ability to collect messages while unattended.
Good operation at most power levels.
Not limited by station-to-station propagation.
Message logging, and ICS report generation.
Forms and template support.
Wide adoption by EmComm related agencies.

## Slide 4: Winlink Connection Modes
Telnet – Non-radio connection through the Internet. Good
for training (no radio equipment required) and use if radio is down or network is busy.
VHF/UHF Packet (local LOS propagation) –
  9600 baud – Fast, reliable, range limited and requires $400
modem (Kantronics or SCS Tracker).
  1200 baud – Slower, but can use inexpensive Byonics TinyTrak-4, TNC-X, or soundcard modems.
HF WINMOR – “Poor man’s Pactor”. Not as good as Pactor, but operates with inexpensive sound card device ($100), speed between Pactor 2 and 3.
HF Pactor 1, 2, 3 and 4 – Fast and reliable but requires an expensive modem ($1500+).

## Slide 5: RMS Express Main Screen
.
Multiple call signs
Personal message folders
Contacts address book
Connection Mode
Standard
Folders
Begin connection

## Slide 6: Composing A Message
New Message Button
Post to Outbox
Multiple recipients and CC
File attachments
Click “To” or “CC” for contacts
Request
Read
Receipt

## Slide 7: Address Book Support
Use of Standard Addresses for EMCOMM is Encouraged

## Slide 8: Using Group Addresses
Click “Files” followed by “Group Address…”
Use a group name in the “To” or “CC” fields

## Slide 9: Tactical Address Support
Adding additional call signs

## Slide 10: Tactical Address Support
Contact info will be duplicated, update or clear these fields

## Slide 11: Tactical Address Support
Use of Tactical Addresses for EMCOMM is Encouraged

## Slide 12: Tactical Address Support
Use of Tactical Addresses for EMCOMM is Encouraged

## Slide 13: Creating Message Templates
Fills in “boilerplate” information for messages
Click “Message” followed by “Templates…”

## Slide 14: Using a Message Template
Begin composing a message
Click “Select Template” and select the template
Click to select a template
CC and subject filled in automatically
Body initialized from template
Favorite templates

## Slide 15: Using a Message Template
Prompting for input

## Slide 16: Using a Message Template
Completed message ready to send

## Slide 17: Message Attachments
File size must be managed

## Slide 18: Message Attachments
Resize and crop pictures within RMS Express

## Slide 19: Pending Message In Outbox
Open Session

## Slide 20: Reading Incoming Messages

## Slide 21: Notification of Read Acknowledgement

## Slide 22: Message Receipt Acknowledgements
Positive acknowledgment that message was received
Information about message filled in automatically

## Slide 23: RMS Express Message Review
Review pending messages before downloading.
Select which messages to download.
Message too large & not wanted

## Slide 24: RMS Express HTML Forms
HTML forms are efficient and professional looking.
Forms can be simple or very complex.
Forms can look as good as any web site.
Forms are easy to use.
Attractive forms are difficult to create unless you understand HTML, cascading style sheets and JavaScript.
The Winlink team is building a library of forms.
Good HTML/JavaScript programmers are needed!

## Slide 25: HTML Form and Template Set
A full form set has three components:
  A template that displays the form and generates the text message to be sent.
  An input form that solicits input from the user.
  A display form that formats and displays the information on the recipient’s computer.
Input from a form is encapsulated in a compact XML file attached to the message.
The actual form HTML is not transmitted.
Input and display forms may be large, but the actual data transmitted is very compact.
Receiving station must have the display form installed.

## Slide 26: RMS Express Forms ICS form for data entry in browser

## Slide 27: RMS Express Forms Completed form ready to send
Plain text version
Captured data entry

## Slide 28: Available RMS Express Forms (ICS)
ICS 205 V1.26 Incident Communications Radio Plan
ICS 205A V1.4 Communications List
ICS 206 V2.1 Medical Plan
ICS 213 V2.36 General Message
ICS 213RR V1.3 Resource Request Message
ICS 214 V2.2 Activity Log
ICS 217A V1.6 Communications Resource Availability Worksheet
All ICS forms are now available in one zip file: http://winlink.org/content/all_ics_forms_one_zip_file_v11

## Slide 29: Available RMS Express Forms (general)
HICS-ICS213 V2.6 General Message
IARU V1.17 Radiogram
ISNAP V1.0 Incident Snapshot for Counties / Tribal Nations
RMSE V1.5 Hospital Bed Report (Marion County FL)
RMSE V1.1 Clay County FL ICS 213
RMSE V1.4 POD General Message Form
RMSE V1.5 Bulletin Form
RMSE V1.5 Simple Message
RMSE V1.6ES Simple Message Spanish Version
RMSE V1.8 Float Plan
RMSE V2.0 Winlink Operator Check In

## Slide 30: Initial Packet Setup Sound Card Virtual TNC
Make sure your Virtual TNC server TCP ports do not conflict with the RMS Express forms server port.

## Slide 31: Winlink Peer-To-Peer Radio-Only Operation
Peer-to-peer: direct radio connection between end-users.
The Internet is not used, all communication by radio.
Only the two client stations are involved.
100% error-free transmission and file attachments.

## Slide 32: P2P Message Set to P2P, addressed to receiving station
Must be addressed to P2P partner

## Slide 33: Packet P2P Session Log Connect, login, send message, log off

## Slide 34: Using the Local Network Local Packet Gateway Stations

## Slide 35: Using the Local Network Local Packet Gateway Stations, nodes and digipeaters

## Slide 36: Using the Local Network Digipeaters and Nodes
Digipeaters can be used to extend the line-of-sight path to a Gateway or P2P partner. Any station can function as a digi if properly configured. Lower level sites are actually better than mountain top sites. Each hop through a digi decreases performance, multiple hops can slow transfer speeds considerably.

## Slide 37: Using the Local Network Digipeaters and Nodes
Complex connections through Nodes can be created using connection scripts. Scripts issue commands and wait for the appropriate response. Nodes provide better performance over multi-hop paths, but there is still a significant performance penalty.
Scripts can be simple or very complex. Detailed knowledge of the network is required.

## Slide 38: Using the Local Network Digipeaters and Nodes
Waiting for the correct response
These are expected errors parsing for the correct response
End of script, the connection now continues normally

## Slide 39: Using the Local Network Digipeaters and Nodes
Using nodes and digis has a significant impact on throughput
Requires a good knowledge of available resources
May require adjustment of packet parameters
Be aware of the “hidden terminal” issue
Full duplex digital repeaters are a better solution
  There is only 1 available, in Snohomish
You cannot run voice and data on the same band at the same time from the same location. We need to have voice and data on different bands.

## Slide 40: Winlink Radio-Only Network Local networks connected by HF, regional or long distance
Local Users
Local Users
Local Users
Geographically
Separated

## Slide 41: Catalog Information Requests
Use the “Winlink Catalog Request” feature in RMS
Express to request:
  Weather maps for most areas of the world.
  Weather forecasts.
  Maritime HF nets and frequencies.
  Satellite images.
  Location of closest 30 stations.
  ARRL Newsletter, e-letter, etc.
  Misc. bulletins.

## Slide 42: RMS Express Query Catalog

## Slide 43: Weather Map Image Returned for Request

## Slide 44: Winlink Position Reports
You can send position reports to the Winlink system.
  Coordinates sent via connected GPS.
  Otherwise, your position may be entered manually.
Position Reports are sent to:
  Winlink system map.
  ShipTrak maps.
  APRS maps.
  YotReps maps.
Extremely valuable for pinpointing locations, especially for maritime operation.

## Slide 45: Posting a Position Report
Data from a connected GPS unit.
WX
assistance to the NWS Voluntary Marine Observation Program.
Useful in tracking with e-mailed disaster assessments.

## Slide 46: Winlink.org Real-time Position Report Page

## Slide 47: RMSMessageLog ICS-309 Generator
Messages during period
Select folders
Starting & ending report period
Generate ICS-309
pdf file

## Slide 48: Generated ICS-309 PDF Message Log Report

## Slide 49: Future Development Amateur Radio Digital Open Protocol (ARDOP)
The ARDOP project is a joint development effort among amateur radio developers that seeks to provide a specification and implementation (software or hardware) for a modern versatile open digital protocol.
Replaces Winmor, AX.25 Packet, ???
Soundcard based, or open hardware platform

## Slide 50: Future Development Amateur Radio Digital Open Protocol (ARDOP)

## Slide 51: Conclusion
Winlink use continues to grow, especially for EmComm.
The Winlink Development Team continues to enhance capabilities to adapt to changing needs.
RMS Express is the recommended client application
  Familiar e-mail like user interface
  Flexible connection options
  HTML form support
  Used by most local teams